Notes on Z80 Macro Generation

Z80 code is generated using a semi automatic system. It produces several files.

I am deliberately not taking advantage of the IX/IY substitution.

opcodes.h	Opcodes for base statements
opcodesdd.h	Opcodes for DD/FD statements
opcodesed.h	Opcodes for ED statements
opcodescb.h	Opcodes for CB statements
opcodesddcb.h	Opcodes for DDCB and FDCB statements (a pointer to IX/IY is set)
opmacros.h	All #define lines
opsource.h	All other lines.

These are generated from macro files. There are two types of these - .inc files which are generic definitions, and .cpu which handle specific groups or subgroups. .inc files can be in a common subdirectory include or in the current directory.

A Python script takes each .cpu file in turn and builds a set of case statements for one of the five source files, and collates date for opmacros.h and opsource.h and then outputs all seven source files.

The definition files (.inc and .cpu) have the same format.

1. A line beginning with # is a comment and is removed
2. A line beginning with : is a macro or source line and is transferred to either the opmacros.h (if it begins with #define) or opsource.h.
3. A line beginning with @ defines a group
4. All other lines define code.

Case is irrelevant (except in the code generated). By convention registers are capitalised, mnemonics and group definitions are lower case.

Group definitions

Group definitions specify multiple substitutions – for example they may represent B,C,D,E,H,L,(HL) or A say. Each optionally has a substitution which overrides the default substitution which is the value itself, and a bit shift. So if you are looking for a source read on on L it may look like the following :-

@SRC { B,C,D,E,H,L,(HL):READ8(HL()),A } : 0

This means that if you have the following as a code line.

40 4	LD A,@SRC
A = @SRC

It will generate the following opcode, mnemonic and code commands (all of which are currently 4 cycles ; it’s approximate, I might make R/W bump cycles or scan for it)

40	LDA A,B	A = B ; CYCLES(4);break
41	LDA A,C	A = C ; CYCLES(4);break
..
46	LD A,(HL)	A = READ(HL()) ; CYCLES(4);break
47	LD A,A	A = A ; CYCLES(4);break

If the shift was (say) 3 they would go in 40,48,50,58 etc.

Multiple definitions can go in the same opcode and they will generate all combinations.

Because of R/W you cannot use Right Hand side values. Normally the save value will go into MBR and the subsitution will write this. e.g.

@DEST { B:B=MBR ; …. ; (HL):WRITE8(HL(),MBR) ; A=MBR }

Word Definitions

Word definitions begin with a non tabbed line, and all the following tabbed lines belong to it, so its a pythonic syntax

<base opcode> <cycle count> <mnemonic>
<code line 1>
<code line 2>

base opcodes can be 00-FF DD00-DDFF ED00-EDFF CB00-CBFF and DDCB00-DDCBFF. Code normally uses correct register names, except the alternate set use Alt_B for B. When accessing code for IX IY there is a variable *ip which points to either IX or IY accordingly.

Some opcodes have an operand between the instructions, all (I think) IX displacements. DDCB <disp> <opcode> In this case, the sign extended displacement is in iDisp and it done in the original dispatcher (e.g. there is a dispatcher in opcodedd.h for CB, which fetches it)